## Slide 1: Importance of the Contributing Zone when Protecting the Edwards Aquifer
Bexar Audubon Society
Ronald T. Green, Ph.D., P.G.
Southwest Research Institute®
July 22, 2020

## Slide 2
Edwards Aquifer Protection Plan
Background

## Slide 3: City of San Antonio Edwards Aquifer Protection Program
Residents of San Antonio have passed four propositions:
Proposition 3: 2000: 1/8 cent sales tax ($45M) to buy sensitive properties over Edwards Aquifer Recharge Zone in Bexar County, established SET and CAB
Proposition 1: 2005: 1/8 cent sales tax ($90M) continuation, added other counties
Proposition 1: 2010: 1/8 cent sales tax ($90M) continuation
Proposition 1: 2015: 1/8 cent sales tax ($90M+10M) continuation, add $10M for Demonstrations Projects within Bexar County
Future ?????

## Slide 4: How are properties identified and acquired in EAPP?
Scientific Evaluation Team (SET)
Conservation Advisory
Board (CAB)
COSA City Council
Land Acquisition
Team (LAT)

## Slide 5: City of San Antonio Edwards Aquifer Protection Program
Scientific Evaluation Team (SET): scientific experts prioritize properties based on their environmental characteristics to achieve maximum value for voter-approved dollars. → SET Model

## Slide 6: City of San Antonio Edwards Aquifer Protection Program
Land Acquisition Team (LAT) visits properties identifying that may be considered for the conservation easement program.

## Slide 7: City of San Antonio Edwards Aquifer Protection Program
Conservation Advisory Board (CAB) Takes all information, including SET Model and makes decision on which properties to protect by purchase or conservation easement.
Makes recommendation to COSA City Council

## Slide 8: City of San Antonio Edwards Aquifer Protection Program
COSA City Council votes whether to approve CAB recommendation

## Slide 9: Mostly Exclusive to the Edwards Aquifer Recharge Zone: Limited Extension into the Contributing Zone

## Slide 10: Properties Protected by the Edwards Aquifer Protection Plan (EAPP)

## Slide 11: City of San Antonio Edwards Aquifer Protection Program
Contentious Debate on the EAPP

## Slide 12: City of San Antonio Edwards Aquifer Protection Program
Contentious Debate on the EAPP
Has the EAPP done all it was meant to do?

## Slide 13: City of San Antonio Edwards Aquifer Protection Program
Contentious Debate on the EAPP
Has the EAPP done all it was meant to do?
Is there more that the EAPP should do?

## Slide 14
Edwards Aquifer
Source: Edwards Aquifer Authority 2008

## Slide 15
Edwards Aquifer
Contributing Zone
Recharge Zone
Confined Zone
Source: Edwards Aquifer Authority 2008

## Slide 16: The Real Question
How important is protecting the Edwards Aquifer Contributing Zone to protecting the quality of recharge to the Edwards Aquifer?

## Slide 17: Answer
If the Contributing Zone is (critically) important to protecting the recharge to the Edwards Aquifer…

## Slide 18: Answer
If the Contributing Zone is (critically) important to protecting the recharge to the Edwards Aquifer…
…then if you aren’t protecting the Contributing Zone, you aren’t protecting the Edwards Aquifer

## Slide 19
Source: Edwards Aquifer Authority 2008
Edwards Aquifer
Conventional Conceptualization

## Slide 20: The Edwards Plateau Was Formed by Sea Sediments that Solidified Then Lifted Over 10s of Millions of Years

## Slide 21
Source: Edwards Aquifer Authority 2008
Edwards Aquifer
Conventional Conceptualization

## Slide 22: Autogenic Recharge (Derived from Within)
Contributing Zone
Confined Zone
Recharge Zone

## Slide 23: Allogenic Recharge (Derived from Yonder)
Contributing Zone
Confined Zone
Recharge Zone

## Slide 24: Allogenic + Autogenic Recharge (Derived from Within and from Yonder)
Contributing Zone
Confined Zone
Recharge Zone

## Slide 25: Allogenic + Autogenic Recharge (Derived from Within and from Yonder)
Contributing Zone
Recharge Zone
Confined Zone
Conventional
Conceptualization

## Slide 26
There is considerable evidence that the
Contributing Zone is way more important than previously believed

## Slide 27
There is considerable evidence that the
Contributing Zone is way more important than previously believed
A quick demonstration…Helotes Creek watershed

## Slide 28
Medina River
Watershed
San Antonio River
Watershed

## Slide 29
Leon Creek
Watershed

## Slide 30
Helotes Creek
Watershed

## Slide 31
Contributing
Zone
Recharge
Zone
Artesian
Zone
I-10
1604
Hwy 16

## Slide 32
Conducted Gain/Loss Study of Helotes Creek

## Slide 33
Lower Helotes Creek Sub-Basin
0.94 cfs
3.05 cfs
2.47 cfs
Chimenia
Creek
Lee Creek
Helotes Creek
1.06 cfs
0.00 cfs
4.24 cfs
Los Reyes
Creek
Edwards Aquifer
Recharge Zone
Edwards Aquifer
Contributing Zone
Helotes Creek

## Slide 34
Lower Helotes Creek Sub-Basin
0.94 cfs
3.05 cfs
2.47 cfs
Chimenia
Creek
Lee Creek
Helotes Creek
1.06 cfs
0.00 cfs
4.24 cfs
Los Reyes
Creek
Edwards Aquifer
Recharge Zone
Edwards Aquifer
Contributing Zone
Helotes Creek
Helotes Creek Contributing Zone

## Slide 35
Lower Helotes Creek Sub-Basin
0.94 cfs
3.05 cfs
2.47 cfs
Chimenia
Creek
Lee Creek
Helotes Creek
1.06 cfs
0.00 cfs
4.24 cfs
Los Reyes
Creek
Edwards Aquifer
Recharge Zone
Edwards Aquifer
Contributing Zone
Helotes Creek
Helotes Creek looking downstream toward
Recharge Zone
Helotes Creek Contributing Zone
Location of USGS river gauging station

## Slide 36: USGS River Gage on Helotes Creek Upstream of Recharge Zone (cfs) 2010-2011
Date of
gain/loss
survey
Helotes Creek has continuous flow in the Contributing
Zone except for drying out once every 5-7 years.
Flow in Helotes Creek only reaches the Recharge Zone
during periods of heavy precipitation.

## Slide 37
Helotes Creek is not an outlier…

## Slide 38
Helotes Creek is not an outlier…
…there is considerable evidence that considerable
recharge to the Edwards Aquifer occurs in the Contributing Zone

## Slide 39: Allogenic + Autogenic Recharge (Derived from Within and from Yonder)
Contributing Zone
Confined Zone
Conventional
Conceptualization
Recharge Zone

## Slide 40: Autogenic + Allogenic Recharge
Contributing Zone
Recharge Zone
Confined Zone

## Slide 41: Autogenic + Allogenic Recharge
Confined Zone
Refined
Conceptualization
Contributing Zone
Recharge Zone

## Slide 42
Source: Edwards Aquifer Authority 2008
Edwards Aquifer
Conventional Conceptualization

## Slide 43
Source: Edwards Aquifer Authority 2008
Edwards Aquifer
Refined Conceptualization

## Slide 44
Source: Edwards Aquifer Authority 2008
Edwards Aquifer
Refined Conceptualization

## Slide 45
How does water get from the Contributing Zone to the Edwards Aquifer

## Slide 46
Source: Edwards Aquifer Authority 2008
Edwards Aquifer

## Slide 47: Rain Water Is Focused into River Beds and Acts as a Mild Acid That Dissolves the Limestone
The preferential flow paths that are formed may be a “pipe”, but it is more likely the flow paths are simply zones of enhanced permeability
Incised River Channels
Preferential Flow Paths
Woodruff and Abbott, 1970s, 1980s

## Slide 48
Development of karst conduits in carbonate aquifers
Woodruff and Abbott, 1979, 1986

## Slide 49: Fast groundwater flow occurs in preferential flow paths aligned with river channels in the Contributing Zone
Streams
Preferential Flow Paths

## Slide 50: …back to the SET Model

## Slide 51: During the first three SETs properties in the Contributing Zone were given little weight in the SET Model

## Slide 52: This changed in 2015, when the 4th SET took into consideration recent science that documented the importance of the Contributing Zone

## Slide 53: Refined Contributing Zone weighting by 4th SET is based on: 1) watershed basin 2) distance from the Recharge Zone 3) distance from the river channel

## Slide 54: Composite weighting assigned to each parcel
= Total weighting assigned to a parcel [0-30]
= Watershed weighting [0-10]
= Distance from recharge zone weighting [0-10]
= Distance from river channel weighting [0-10]
Parcel center is determined using ARCGIS (center of gravity)

## Slide 55: Consideration of Contributing Zone

## Slide 56: The SET recommended extending the EAPP into the Contributing Zone The CAB has been reluctant extending the EAPP into the Contributing Zone

## Slide 57: The <policy maker> has been reluctant extending the EAPP into the Contributing Zone The <technical advisor> continues to recommend extending the EAPP into the Contributing Zone

## Slide 58: Properties Protected by the Edwards Aquifer Protection Plan (EAPP)

## Slide 59: Considerable properties in the Contributing Zone merit protection from development

## Slide 60: Basins are weighted according to impact on San Antonio
No. | Watershed | Weighting
1 | Guadalupe River | 0
2 | Blanco River | 0
3 | Nueces River | 5
4 | Frio River | 6
5 | Medina River | 9
6 | Cibolo Creek | 6
7 | Dry Comal Creek | 5
8 | Sabinal River | 6
9 | Area between Sabinal and Medina rivers | 7
10 | Area between Medina River and Cibolo-Dry Comal Creek | 10
11 | Area west of Nueces-West Nueces rivers | 0
12 | Area south of Nueces-West Nueces rivers | 0
13 | Area between Frio and Nueces rivers | 6
14 | Area between Frio and Sabinal rivers | 6
15 | West of area between Sabinal and Medina rivers | 5
16 | South of area between Sabinal and Medina rivers | 5
17 | West of Medina River | 8
18 | West of area between Medina and Cibolo-Dry Comal Creek | 10
19 | Area between Blanco and Guadalupe rivers | 0
20 | Colorado River-Onion Creek | 0
21 | West Nueces River | 0

## Slide 61: Basins are weighted according to impact on San Antonio
No. | Watershed | Weighting
1 | Guadalupe River | 0
2 | Blanco River | 0
3 | Nueces River | 5
4 | Frio River | 6
5 | Medina River | 9
6 | Cibolo Creek | 6
7 | Dry Comal Creek | 5
8 | Sabinal River | 6
9 | Area between Sabinal and Medina rivers | 7
10 | Area between Medina River and Cibolo-Dry Comal Creek | 10
11 | Area west of Nueces-West Nueces rivers | 0
12 | Area south of Nueces-West Nueces rivers | 0
13 | Area between Frio and Nueces rivers | 6
14 | Area between Frio and Sabinal rivers | 6
15 | West of area between Sabinal and Medina rivers | 5
16 | South of area between Sabinal and Medina rivers | 5
17 | West of Medina River | 8
18 | West of area between Medina and Cibolo-Dry Comal Creek | 10
19 | Area between Blanco and Guadalupe rivers | 0
20 | Colorado River-Onion Creek | 0
21 | West Nueces River | 0

## Slide 62: Primary focus on Contributing Zone to be protected

## Slide 63: City of San Antonio Edwards Aquifer Protection Program
Contentious Debate on the EAPP
Has the EAPP done all it was meant to do?
Is there more that the EAPP should do?

## Slide 64: City of San Antonio Edwards Aquifer Protection Program
Contentious Debate on the EAPP
Has the EAPP done all it was meant to do?
NO
Is there more that the EAPP should do?

## Slide 65: City of San Antonio Edwards Aquifer Protection Program
Contentious Debate on the EAPP
Has the EAPP done all it was meant to do?
NO
Is there more that the EAPP should do?
YES

## Slide 66: Contact Information
Ronald T. Green, Ph.D., P.G.
Technical Advisory
Earth Science Section
Space Sciences and Engineering Division
Southwest Research Institute
6220 Culebra
San Antonio, Texas 78238
1.210.522.5305 (office)
1.210.316.9242 (cell)
rgreen@swri.edu